Commentary on our 'bootmsw.s' program


0.  The ROM-BIOS 'bootstrap function' will load this program into 
    memory at the standard physical address 0x00007C00, then will
    transfer control that location, by simultaneously placing the 
    values 0x0000:0x7C00 into registers CS:IP, respectively.   

1.  The first action that our program takes is to perform a 'far
    jump' instruction, in order to change the value in segment-
    register CS so that the offsets for labels, assigned by the 
    assembler, will match the actual offsets of their locations
    in the code's segment:

			CS <--- 0x07C0
			IP <--- #main  

2.  The next actions taken are to copy the new code-segment value
    into segment-registers DS and ES, so that the normal symbolic
    addressing used in subsequent instructions will be valid.  In
    most cases, instructions that refer to data by using labels
    will automatically use the segment-value from register DS by 
    default, unless an explicit segment-override prefix appears,
    and direct control-transfers (jumps or calls) that refer to 
    labels will automatically use the segment-value from CS.  So
    it might appear that we wouldn't need to initialize register 
    ES.  However, the 'write_string' BIOS service, used later to
    display a character-string on the video screen, expects to
    find that string's address in the ES:BP register-pair.  Thus
    we might as well, for efficiency's sake, go ahead and copy
    our code's segment-address into both DS and ES, to avoid an
    extra step later on.

3.  In principle we could justifiably be criticized for executing
    the LMSW-instruction (i.e., Load Machine Status Word) without 
    first performing a check to make sure our processor is 80286
    or higher, since LMSW was an undefined opcode on an 8086 cpu.
    But for simplicity we omit this check here, as hardly anyone
    has a 8086 machine nowdays, and quite a few extra instructions 
    would be needed to check the processor's model-number, thereby
    obscuring the main ideas in this demo program.

4.  The algorithm we use to develop our message-string consists of
    looping sixteen times, once for each bit in the MSW register,
    extracting a bit and converting it to an ascii code, either
    '0' or '1', for display.  The shift-left instruction ('SHL')
    shifts the most significant bit from register AX to the carry
    flag, then the Add-with-Carry instruction adds zero plus the
    carry-flag to the ascii code for '0' already in register DL.

5.  Once our message-string is ready to be displayed, we perform
    three service-calls to the BIOS firmware in order to place
    our message on the screen at the current cursor-position.
    All three service-callspertain to the video system are made 
    using the int-0x10 (video services) interface.
	function 0x0F (Get video state) puts page-number in BH
        function 0x03 (Get cursor position) puts coordinates in DX
        function 0x13 (Write string) draws our string on the screen

6.  The last action is to 'freeze' our program, giving the viewer
    time to examine our message, and then to remove the diskette
    and reboot the machine with a real operating system, so that
    further program development can be done using the OS tools.

7.  The last action is to 'freeze' our program, giving the viewer
    time to examine our message, and then to remove the diskette
    and reboot the machine with a real operating system, so that
    further program development can be done using the OS tools.

8.  There is one more point of criticism that can legitimately be
    made against this demo program.  It concerns our carelessness
    with regard to the stack.  Our program assumes it can safely
    continue using whatever stack got inherited from the ROM-BIOS
    bootstrap function.  This is probably ok here, since we don't
    use the stack for anything other than normal processing of
    device interrupts (e.g., the system timer) and service-calls
    to the three ROM-BIOS video routines.  However, it cannot be
    denied that there's some risk of a system crash due to stack
    overflow whenever we use a stack of unknown size and location.
    A more correct programming approach, and one that is normally
    taken by nearly every professionally-written boot-loader, is
    to include a code-fragment at the beginning of our program to
    establish a stack-area of a known size and memory-location;
    for example, like this:

			xor  ax, ax
			mov  ss, ax
			mov  sp, #0x7C00

    Here we note that we are relying on Intel's documented behavior
    for instructions that modify register SS without simultaneously
    modifying register SP, namely, that interrupts are temporarily
    masked automatically until after the instruction that follows
    has completed its execution, because otherwise the sequence 

			mov  ss, ax
			mov  sp, #0x7C00

    would constitute a "critical section" of code, risking a system
    crash if an interrupt were to occur while the stack-pointer was
    only part-way modified.  It is reported that some steppings of
    early CPUs did not properly implement this temporary interrupt
    masking, so knowledgable programmers frequently bracketed this
    kind of code-fragment with an explicit CLI/STI instruction-pair: 

			cli
			xor  ax, ax
			mov  ss, ax
			mov  sp, #0x7C00
			sti

    But to eliminate this issue entirely, Intel has introduced a new
    instruction that modifies both SS and SP simultaneously:

			lss  sp, newtos

    Here 'newtos' is the label for a double-word memory-value where
    new offset and segment addresses have been stored in advance:

		newtos: .WORD  0x7C00, 0x0000

    Of course, one would need to include a check in advance to make
    sure the processor implements this new instruction; if not, it
    likely would crash when this undefined opcode got fetched.  But
    since our classroom machines use Pentium 4 processors, we could 
    omit such a check, so long as we could be certain that our code 
    would never get executed on any outside machines.